Deming Public Schools

Parade Float Safety

1. Float & Running Gear – The foundation for a tow float is typically a sturdy flat trailer bed with pneumatic wheels. All load supporting areas on the float should be wood, steel or other structurally competent material (not cardboard). Wheels, tires, dollies, axels, bearings of adequate sizes and strength to support the total load of the float are required. Wheels and tires must be in good condition

and vehicle brakes sufficient to stop the float when loaded. The authority having jurisdiction with the parade shall have the right exclusive right to ban any unsafe vehicle.

2. Vehicle Maintenance – Vehicles pulling floats shall be serviced for gas, oil, water, tires and battery prior to reporting to the staging area. Vehicles licensed for highway use shall provide the inspecting official with proof of insurance. No extra gasoline may be carried on the float. For emergencies, a horn or other sounding device is to be present.

3. Driver Vision/Communication – Floats decorations shall be designed to allow the driver 180 degrees clear vision to the front and sides of the float or tow unit. If 180 degrees vision cannot be provided, a spotter(s) with clear vision of these areas must accompany the float as a guide. Drivers shall also have clear view of (or communication with) float riders in the event of a problem on that float.

4. Fire Extinguisher – At least one (1) 10 pound ABC fire extinguisher shall be carried in a easily accessible, designated location on the float or tow vehicle. The fire extinguisher shall be sealed, tagged, and dated with in the previous 12 – month period. Open flame displays, roman candles, and fire works are prohibited on floats and tow vehicles.

5. Rider Safety – All participants riding on floats shall have solid sitting arrangement with hand holds readily available to them. Any standing participant shall have a stabilized body support with buckled safety belt or other means to prevent falling from the unit. No person shall be wired or tied to the float. Secured safety rails, barriers, or ropes may be used to prevent a fall from the float. Safety rails and

barriers are to a minimum of 36” tall. No unsecured riders may be located where they might fall beneath the float, its wheels or between the tow vehicle and float (e.g. no seating on rear edge of tow vehicle or on front edge of float). If present, children must be under adult supervision and seated at all times when in motion. Alcohol consumption or smoking on the float is prohibited.

6. Driver – Float drivers shall have a valid driver’s license for the vehicle towing the float and be in competent condition to safely operate the vehicle. Driving under the influence of drugs or intoxicants is prohibited. For the safety of float riders, the driver must minimize abrupt starts and stops. The float safety checklist must be in the possession of the driver.

7. Generators – Where used, generators shall be securely mounted on the vehicle with not less than 12” inches of clearance separating it from any combustible material. Any generator in a confined space (e.g. pick-up camper shell) shall not have any riders inside the same space

.

8. Electrical System – Where used for lighting, motorized decorations or other applications on a float, electrical wiring must be of a type approved for the use for which it is being employed, shall have sufficient capacity, shall be secured to prevent damage, shall have all connections secured via approved devices ( or electrical boxes ) and shall be properly fused. No bare wires or exposed electrical

connections are permitted.

9. Speed – Towed floats shall be capable of maintaining a minimum speed of 10 miles per hour during the parade. The speed when the float is occupied during the parade is limited to a maximum of 5 miles per hour.

10. Towing Safety – Adequate primary (tow bar) and secondary connections (chains, cable, etc) devices shall be made between the towing vehicle and float. All connections shall comply with any and all applicable laws and standards. Primary and secondary connections shall be appropriate for the normal and anticipated loads.

11. General Safety – Hard objects, candy boxes, etc, should not be thrown from the float during the parade. Parade participants wishing to provide give- aways should have walkers along the float to HAND OUT the give-aways. DO NOT THROW ITEMS INTO THE CROWD.

Inspection

All floats will be subject to an inspection check for compliance with the float safety requirements prior to commencement of a parade. The float safety checklist must be signed and in the possession of the driver at the start of the parade.

Created by DPS Safety Office 11-17-09